## Slide 1: Advanced Electrical The 35 Most Missed & Misunderstood Electrical Inspection Items
Dave Haught, ACI, MIES, EP

## Slide 2: The 35 Most Missed & Misunderstood Electrical Inspection Items
I want to avoid a boring two hour long-dry lecture….
With participation, I believe we can have an exciting informational and enjoyable two hours.
Answer with a show of hands…..

## Slide 3: The 35 Most Missed & Misunderstood Electrical Inspection Items
T F 1. The National Electrical Code is written with clear explanatory language so that it can meet the intent of being understood by persons without specialized training.

## Slide 4
T F 1. The National Electrical Code is written with clear explanatory language so that it can meet the intent of being understood by persons without specialized training.
False
NEC 2014 [90.1(C)] “The NEC is a set of rules. Not a set of explanations”

## Slide 5: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s Start outside at the service drop or service lateral.
All of you are aware of the depth of underground service laterals 24 inches and 36 under driveways…..
And we learned the heights for Service Drops

## Slide 6: The 35 Most Missed & Misunderstood Electrical Inspection Items
And we learned the heights for Service Drops

## Slide 7: The 35 Most Missed & Misunderstood Electrical Inspection Items
We all understand that we have three conductors to the home on a single phase service. Two Hot (120 volt) and a neutral.

## Slide 8: The 35 Most Missed & Misunderstood Electrical Inspection Items
What would you rather loose one of the two hot. (loosing ½ the power in the home) or the neutral? (The home would rely on the grounding system to complete the circuit)
Show of hands Hot?
Neutral?

## Slide 9: The 35 Most Missed & Misunderstood Electrical Inspection Items
Lets think about where the electric flows in the circuit.

## Slide 10: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s Start with the toaster or any appliance in the home.

## Slide 11: The 35 Most Missed & Misunderstood Electrical Inspection Items
The electrical flow starts at the generation plant.
Goes through the distribution system to a Transformer in your neighborhood

## Slide 12: The 35 Most Missed & Misunderstood Electrical Inspection Items
The electrical flow continues along utility electric lines until it reaches your home

## Slide 13: The 35 Most Missed & Misunderstood Electrical Inspection Items
The electrical flow continues along utility electric lines until it reaches your home

## Slide 14: The 35 Most Missed & Misunderstood Electrical Inspection Items
The electrical flow continues along utility electric lines until it reaches your home

## Slide 15: The 35 Most Missed & Misunderstood Electrical Inspection Items
The electrical flow continues along utility electric lines until it reaches your home through a lateral drop

## Slide 16: The 35 Most Missed & Misunderstood Electrical Inspection Items
Then through the main panel and to the toaster

## Slide 17: The 35 Most Missed & Misunderstood Electrical Inspection Items
Then through the main panel and to the toaster

## Slide 18: The 35 Most Missed & Misunderstood Electrical Inspection Items
So this is what we get…..

## Slide 19: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric
Back to its source the transformer

## Slide 20: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 21: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 22: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 23: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 24: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 25: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 26: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 27: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric
Toaster heats Toast pops up

## Slide 28: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric
Toaster heats Toast pops up
Circuit starts Return trip

## Slide 29: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 30: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 31: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 32: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 33: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 34: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 35: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 36: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 37: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 38: The 35 Most Missed & Misunderstood Electrical Inspection Items
Normal Circuit flow of electric

## Slide 39: The 35 Most Missed & Misunderstood Electrical Inspection Items
The Circuit is “completed” at the Transformer

## Slide 40: The 35 Most Missed & Misunderstood Electrical Inspection Items
Circuit is “completed” at the Transformer

## Slide 41: The 35 Most Missed & Misunderstood Electrical Inspection Items
What Happens if one of the two Hot lateral Wires are Cut?

## Slide 42: The 35 Most Missed & Misunderstood Electrical Inspection Items
What Happens if one of the two Hot lateral Wires are Cut?
Show of hands….
Nothing? Toast

## Slide 43: The 35 Most Missed & Misunderstood Electrical Inspection Items
What Happens if one of the two Hot lateral Wires are Cut?
Show of hands….
No Toast?

## Slide 44: The 35 Most Missed & Misunderstood Electrical Inspection Items
Picture in your mind what we have….
Remember we have two hot (120v) service laterals.
It depends which one is cut.

## Slide 45: The 35 Most Missed & Misunderstood Electrical Inspection Items
Picture in your mind what we have….
Remember we have two hot (120v) service laterals.
It depends which one is cut.
You had a 50/50 chance of being right...

## Slide 46: The 35 Most Missed & Misunderstood Electrical Inspection Items
Picture in your mind what we have….
Remember we have two hot (120v) service laterals.
It depends which one is cut.

## Slide 47: The 35 Most Missed & Misunderstood Electrical Inspection Items
OK What Happens, if the neutral wire to the Toaster is Cut?
(between receptacle & Toaster)

## Slide 48: The 35 Most Missed & Misunderstood Electrical Inspection Items
What Happens if the neutral wire to toaster is Cut?
Show of hands….
Nothing? Toast

## Slide 49: The 35 Most Missed & Misunderstood Electrical Inspection Items
What Happens if the neutral wire to toaster is Cut?
Show of hands….
Nothing? Toast

## Slide 50: The 35 Most Missed & Misunderstood Electrical Inspection Items
No Toast
What happened if the neutral wire to the toaster is Cut?

## Slide 51: The 35 Most Missed & Misunderstood Electrical Inspection Items
What Happens if the neutral on the overhead service lateral is broken or cut ?

## Slide 52: The 35 Most Missed & Misunderstood Electrical Inspection Items
Tell – Tell Signs of cut or broken Neutral

## Slide 53: The 35 Most Missed & Misunderstood Electrical Inspection Items
No drip loop-hot conductors with tension

## Slide 54: The 35 Most Missed & Misunderstood Electrical Inspection Items
No drip loop-hot conductors with tension

## Slide 55: The 35 Most Missed & Misunderstood Electrical Inspection Items
Cut or broken Neutral

## Slide 56: The 35 Most Missed & Misunderstood Electrical Inspection Items
OK What Happens, if the neutral is broken or cut?
Cut or broken Neutral

## Slide 57: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s return to our trusty Toaster example.

## Slide 58: The 35 Most Missed & Misunderstood Electrical Inspection Items
What Happens if the neutral lateral wire is Cut?
Show of hands….
Nothing? Toast

## Slide 59: The 35 Most Missed & Misunderstood Electrical Inspection Items
What Happens if the neutral lateral wire is Cut?
Show of hands….
No Toast

## Slide 60: The 35 Most Missed & Misunderstood Electrical Inspection Items
Toast
What Happens if the neutral wire to toaster is Cut?

## Slide 61: So…Who Cares? We got toast!

## Slide 62: The 35 Most Missed & Misunderstood Electrical Inspection Items
Remember current flows from the transformer…..

## Slide 63: The 35 Most Missed & Misunderstood Electrical Inspection Items
Back to its source the transformer
Current flows along the electrical lines

## Slide 64: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines

## Slide 65: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines

## Slide 66: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines

## Slide 67: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines

## Slide 68: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines

## Slide 69: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines

## Slide 70: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines

## Slide 71: The 35 Most Missed & Misunderstood Electrical Inspection Items
Toaster heats Toast pops up
Current flows along the electrical lines

## Slide 72: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines In the house to the panel
Toaster heats Toast pops up Circuit starts Return trip

## Slide 73: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines In the house to the panel

## Slide 74: The 35 Most Missed & Misunderstood Electrical Inspection Items
Current flows along the electrical lines In the house to the panel

## Slide 75: The 35 Most Missed & Misunderstood Electrical Inspection Items
BUT The neutral to the transformer is cut / broken !

## Slide 76: The 35 Most Missed & Misunderstood Electrical Inspection Items
STOP
BUT The neutral to the transformer is cut / broken !

## Slide 77: The 35 Most Missed & Misunderstood Electrical Inspection Items
Unlike the toaster cord there is an alternate neutral path to the transformer
STOP

## Slide 78: The 35 Most Missed & Misunderstood Electrical Inspection Items
The path has to be the home’s grounding system

## Slide 79: The 35 Most Missed & Misunderstood Electrical Inspection Items
Neutral’s path to ground with a lot of resistance

## Slide 80: The 35 Most Missed & Misunderstood Electrical Inspection Items
Neutral’s path to ground with a lot of resistance

## Slide 81: The 35 Most Missed & Misunderstood Electrical Inspection Items
Neutral’s path to ground with a lot of resistance

## Slide 82: The 35 Most Missed & Misunderstood Electrical Inspection Items
Neutral’s path to ground with a lot of resistance

## Slide 83: The 35 Most Missed & Misunderstood Electrical Inspection Items
Neutral’s path to ground with a lot of resistance

## Slide 84: The 35 Most Missed & Misunderstood Electrical Inspection Items
Neutral’s path to ground with a lot of resistance

## Slide 85: The 35 Most Missed & Misunderstood Electrical Inspection Items
The circuit is “Complete”

## Slide 86: The 35 Most Missed & Misunderstood Electrical Inspection Items
Is the Resistance in the Soil always the Same?

## Slide 87: The 35 Most Missed & Misunderstood Electrical Inspection Items
What is a better conductor dry soil or wet?

## Slide 88: The 35 Most Missed & Misunderstood Electrical Inspection Items
What is a better conductor Aluminum wire or soil?

## Slide 89: The 35 Most Missed & Misunderstood Electrical Inspection Items
Back to my original question….
What happens when the Neutral Lateral is cut or broken?

## Slide 90: Let’s go to Ohms Law.

## Slide 91: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law.

## Slide 92: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law.

## Slide 93: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law.

## Slide 94: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law.

## Slide 95: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Voltage = Resistance x Current
V = R x I

## Slide 96: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Voltage = Resistance x Current
V = R x I
As an example, let’s say Current (I) amps = 200
Resistance is a value of .6. 200 x.6=120v

## Slide 97: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Voltage = Resistance x Current
V = R x I
As an example, let’s say Current (I) amps = 200
Resistance is a value of .6. 200 x.6=120v
If the Resistance increases to 5 200 x5 =1,000v !

## Slide 98: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Power (Watts) = Resistance x I2
P = R x I2

## Slide 99: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Power (Watts) = Resistance x I2
P = R x I2
Again resistance is .6 and amperage 200
P = .6 x 2002 .6 x 40,000 = 24,000 watts
Resistance is Increased again to 5

## Slide 100: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Power (Watts) = Resistance x I2
P = R x I2
Again resistance is .6 and amperage 200
P = .6 x 2002 .6 x 40,000 = 24,000 watts
Resistance is Increased again to 5
P= 5 x 200 5 x 40,000 = 200,000 watts !

## Slide 101: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Current = Voltage / Resistance
I = V / R
Voltage = 120v Resistance is a value of .6

## Slide 102: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Current = Voltage / Resistance
I = V / R
Voltage = 120v and Resistance is a value of .6 120 / .6 = 200

## Slide 103: The 35 Most Missed & Misunderstood Electrical Inspection Items
Let’s go to Ohms Law
Current = Voltage / Resistance
I = V / R
Voltage = 120v and Resistance is a value of .6 120 / .6 = 200
Resistance increases to 5
120 / 5 = 24 See the drop in current!

## Slide 104: The 35 Most Missed & Misunderstood Electrical Inspection Items
So, what does this mean?
Half of the home will have a drop in watts incandescent lights will be dimming.
The other half will show a huge increase ½ the incandescent lights will be very bright and burning out.
SO ???

## Slide 105: The 35 Most Missed & Misunderstood Electrical Inspection Items
IT CAN CAUSE A HOUSE FIRE!

## Slide 106: What is Stray Voltage?

## Slide 107: Why do we have Stray Voltage?

## Slide 108: Where does Stray Voltage come from?
How and where do I measure stray voltage?
Does Grounding/Bonding take Stray Voltage to zero volts?

## Slide 109: The 35 Most Missed & Misunderstood Electrical Inspection Items
Would you be surprised to learn if you take a voltage meter (analog) and connect one lead to your gas meter and the other to earth, or your water pipe to earth, or even your swimming pool ladder to earth you will get a voltage reading. This is stray voltage.

## Slide 110: The 35 Most Missed & Misunderstood Electrical Inspection Items
I can remember being in the 7th trade making a Crystal Radio to listen to the World Series. I hid the radio components in a hole cut out of the center of an old book. The antenna was a wire dropped at lunch from a second floor classroom window. I sat near the window and I could alligator clip on the radiator to ground and get the stray current to powered the radio.

## Slide 111: The 35 Most Missed & Misunderstood Electrical Inspection Items

## Slide 112: What is Stray Voltage?
Why do we have Stray Voltage?
Where does Stray Voltage come from?

## Slide 113: The 35 Most Missed & Misunderstood Electrical Inspection Items
What is Stray Voltage?
Stray voltage is the occurrence of electrical potential between two objects that ideally should not have any voltage difference between them. Small voltages often exist between two objects in separate locations, due to normal current flow in the power system

## Slide 114: The 35 Most Missed & Misunderstood Electrical Inspection Items
Why do we have Stray Voltage?
Where does Stray Voltage come from?
Let’s go back to our trusty toaster example. We all understand there is resistance in the wires. Based on distance and the size of the wire (AWG) and distance, there will be a voltage drop. The amount of voltage drop from the transformer to your home will show up as stray voltage.

## Slide 115: Stray Electric… Big Deal! Why should I care?

## Slide 116: You are responsible, during your inspections, to insure the electrical system is properly grounded and bonded.

## Slide 117: The 35 Most Missed & Misunderstood Electrical Inspection Items
One reason is if water lines are not properly bonded you may feel stray current (shock) getting into the bath or swimming pool.
If your gas lines are not bonded, especially CSST, you could end up with ……

## Slide 118: The 35 Most Missed & Misunderstood Electrical Inspection Items
One reason is if water lines are not properly bonded you may feel stray current getting into the bath or swimming pool.
If your gas lines are not bonded, especially CSST, you could end up with ……

## Slide 119: The 35 Most Missed & Misunderstood Electrical Inspection Items
One reason is if water lines are not properly bonded you may feel stray current getting into the bath or swimming pool.
If your gas lines are not bonded, especially CSST, you could end up with ……

## Slide 120: The 35 Most Missed & Misunderstood Electrical Inspection Items
WITH A HOUSE FIRE!

## Slide 121: The 35 Most Missed & Misunderstood Electrical Inspection Items
Who can tell me what the difference is between grounding and bonding?
Show of hands

## Slide 122: The 35 Most Missed & Misunderstood Electrical Inspection Items
For premises' systems that operate under 600V, grounding “Does Not":
Assist in clearing a line-to-case fault because of its high resistance (IEEE 142 - 2.1.4 and 4.1.1)
Establish a "zero system reference"
Reduce shock hazard to a safe value (IEEE 142 - 2.2.8)
Grounding does provide a path to the earth for:
  Lightning
  Static electricity
  High-frequency noise

## Slide 123: The 35 Most Missed & Misunderstood Electrical Inspection Items
Bonding Summary
For premises' systems that operate under 600V, bonding the system to metal parts does:
  Stabilize the system voltage to referenced metal parts [IEEE 142 - 1.5.2.]
  Assist in clearing a line-to-case fault [250.4(A)(3), (4) and (5)]
  Establish a "zero system reference" (IEEE 142 - 2.2.8)

## Slide 124: The 35 Most Missed & Misunderstood Electrical Inspection Items
Who can NOW tell me what the difference is between grounding and bonding?
One of the thing that make this tough is the NEC National Electrical Code itself. The NEC many times uses “grounding” when it really means “bonding”

## Slide 125: The 35 Most Missed & Misunderstood Electrical Inspection Items
When you write your reports, you want to be consistent. Grounding is a wire with the conductors providing an alternative electric path to the earth in an electrical system.

## Slide 126: The 35 Most Missed & Misunderstood Electrical Inspection Items
Bonding is a wire to non normally electric conductors to provide a path to the earth. Example metal water pipes, gas pipes, furnace air ducts, metal buildings, electric panel cabinets.

## Slide 127: How many of you feel comfortable when you walk up to the electric panel for an inspection?

## Slide 128: The 35 Most Missed & Misunderstood Electrical Inspection Items
Your Safety Comes first!
The first thing should do is lightly touch the front of the panel with the back of your hand to ensure the electric panel is not energized.
If you feel that tell-tell electric tingle STOP!
Call in a Qualified Licensed Electrician

## Slide 129: The 35 Most Missed & Misunderstood Electrical Inspection Items
Where is the main panel located?
Show of hands
Outdoors or Indoors ?

## Slide 130: The 35 Most Missed & Misunderstood Electrical Inspection Items
Where is the main panel located?
Show of hands
Outdoors or Indoors ?
Congratulations! You are 100% correct!

## Slide 131: The 35 Most Missed & Misunderstood Electrical Inspection Items
Where is the main panel located?
Show of hands
Outdoors or Indoors ?
The Location does not matter, but it does…..
The location must be a dedicated location with adequate workspace

## Slide 132: The 35 Most Missed & Misunderstood Electrical Inspection Items

## Slide 133: The 35 Most Missed & Misunderstood Electrical Inspection Items

## Slide 134: The 35 Most Missed & Misunderstood Electrical Inspection Items

## Slide 135: The 35 Most Missed & Misunderstood Electrical Inspection Items

## Slide 136: The 35 Most Missed & Misunderstood Electrical Inspection Items

## Slide 137: The 35 Most Missed & Misunderstood Electrical Inspection Items

## Slide 138: The 35 Most Missed & Misunderstood Electrical Inspection Items
What is the difference between a MAIN electrical
Panel and a SUB Panel?

## Slide 139: The 35 Most Missed & Misunderstood Electrical Inspection Items
What is the difference between a MAIN electrical
Panel and a SUB Panel?
The Main Panel is the first panel from the service drop.

## Slide 140: The 35 Most Missed & Misunderstood Electrical Inspection Items
The main panel can be outside at the disconnect or immediately inside.

## Slide 141: Thank you!